This is a mod to mod the CB-radio Dirland DSS9000F with adjustable power for all modes.

- First locate R249 and lift it one side.

- Solder the lifted leg with a wire to one of the outer terminals the 470 Ohm Lin. Potmeter.

- Solder a wire ,where the lifted side of R249 was soldered, also to the adjustment point of the potmeter.(middle terminal)

Be sure that you use the right size potmeter because you have limited space to mount the potmeter on the chassis.

My potmeter was Piherstyle with the casing 16x18 mm !

Choose on the chassis for the right hole to drill for the potmeter ( see photo )